## Slide 1: IETF-115 Hackathon BGP CT: interop experiment #2. JUNOS interop with IOS-XR using SAFI 128
6 Nov 2022
Kaliraj Vairavakkalai

## Slide 2
Concept.
Topology.
Demo.

## Slide 3: Concept
BGP CT uses RFC 8277 and RFC 4364 NLRI encoding, with a new SAFI 76.
So can we demonstrate interop with devices that don’t implement SAFI 76 yet? by using SAFI 128 to carry the BGP-CT routes. Assuming the device is a Transport-only node (Border-Node) which doesn’t need L3VPN service-routes (option-C).
IOS XR Version 6.3.15 (NCS 5500)
  Note: Has L3VPN and SRTE features. But doesn’t support resolving L3VPN over SRTE. It appears that comes in release 6.5.2..
JUNOS private image 23.1I20221103_0534_kaliraj, has a hidden knob “use-safi-128” that:
  Negotiates SAFI 128 in Open message with the BN peer, with an understanding that the routes received will be CT routes.
  Converts SAFI 128 to SAFI 76 during reception of BGP updates. And advertises BGP-CT routes in SAFI-128 Update messages.
This allows achieving end-to-end intent based forwarding where-ever colored-resolution is supported, even if all devices don’t support SAFI-76.
This just demonstrates the ease of implementing BGP CT.

## Slide 4
Concept.
Topology.
Demo.

## Slide 5
AS1
AS2
BGP Service Routes (SAFI 128)
P2
PE1
81.2.2.2
mpls
gold
bronze
best-effort
P1
red.inet
BGP Transport Routes
(SAFI 128)
BGP CT : Junos interop with IOS-XR using SAFI 128
RR2
81.10.10.10
RR1
81.4.4.4
ASBR2 is IOS XR Software, Version 6.3.15. NCS-5500.
ASBR1 and all other nodes are JUNOS 23.1I20221103_0534_kaliraj (with hidden knob “use-safi-128”)
“use-safi-128” is configured at ASBR1, PE2 towards ASBR2.
gold
bronze
best-effort
ASBR1
81.5.5.5
mpls
gold
bronze
best-effort
ASBR2
81.14.14.14
BGP Transport Routes
(SAFI 4)
PE2
81.11.11.11
gold
bronze
best-effort
red.inet
BGP Transport Routes
(SAFI 4)
BGP Transport Routes
(SAFI 128)
(SAFI 76)
(SAFI 128)
BGP Transport Routes
(SAFI 4, 76)
(SAFI 128)
(SAFI 76)

## Slide 6
Concept.
Topology.
Demo.

## Slide 7: Junos: screen capture (1/3)
user@junos-box# show mpls lsp statistics ingress logical-system all
logical-system: P1
Ingress LSP: 3 sessions
To From State Packets Bytes LSPname
81.5.5.5 81.2.2.2 Up 0 0 lsp-PE1-ASBR1
81.5.5.5 81.2.2.2 Up 0 0 lsp-PE1-ASBR1-bronze
81.5.5.5 81.2.2.2 Up 5079185 467285020 lsp-PE1-ASBR1-gold
logical-system: PE2
Ingress LSP: 3 sessions
To From State Packets Bytes LSPname
81.14.14.14 81.11.11.11 Up 0 0 lsp-PE2-ASBR4
81.14.14.14 81.11.11.11 Up 0 0 lsp-PE2-ASBR4-bronze
81.14.14.14 81.11.11.11 Up 5075862 466979304 lsp-PE2-ASBR4-gold
logical-system: default
Ingress LSP: 3 sessions
To From State Packets Bytes LSPname
81.2.2.2 81.5.5.5 Up 0 0 lsp-ASBR1-PE1
81.2.2.2 81.5.5.5 Up 0 0 lsp-ASBR1-PE1-bronze
81.2.2.2 81.5.5.5 Up 5075862 466979304 lsp-ASBR1-PE1-gold

## Slide 8: Junos: screen capture (2/3)
user@junos-box# run show bgp neighbor 13.21.0.21
Nov 07 06:57:00
Peer: 13.21.0.21+179 AS 1 Local: 13.21.0.13+55304 AS 2
Description: Cisco NCS-5500 XR-6.3.15
Group: toAs1-T Routing-Instance: master
Forwarding routing-instance: master
Type: External State: Established Flags: <Sync>
<snip>
Address families configured: inet-labeled-unicast inet-transport
NLRI inet-transport: BgpCTSafi128
<snip>
Local Interface: et-0/0/2.0
NLRI advertised by peer: inet-labeled-unicast inet-transport
NLRI for this session: inet-labeled-unicast inet-transport
NLRI of received end-of-rib markers: inet-labeled-unicast inet-transport
NLRI of all end-of-rib markers sent: inet-labeled-unicast inet-transport
<snip>

## Slide 9: Junos: screen capture (3/3)
user@junos-box# run show route table bgp.transport.3 source-gateway 13.21.0.21
Nov 07 07:07:35
bgp.transport.3: 6 destinations, 6 routes (6 active, 0 holddown, 0 hidden)
Restart Complete
+ = Active Route, - = Last Active, * = Both
81.11.11.11:31:81.11.11.11/96
*[BGP/167] 21:50:46, localpref 100
AS path: 1 I, validation-state: unverified
> to 13.21.0.21 via et-0/0/2.0, Push 24003
81.11.11.11:32:81.11.11.11/96
*[BGP/167] 06:02:54, localpref 100
AS path: 1 I, validation-state: unverified
> to 13.21.0.21 via et-0/0/2.0, Push 24004

## Slide 10: IOS-XR: screen capture (1/2)
RP/0/RP0/CPU0:ncs5508#show bgp neighbor 13.21.0.13
Mon Nov 7 06:42:02.855 UTC
BGP neighbor is 13.21.0.13
Remote AS 2, local AS 1, external link
Description: Junos-23.1I20221103_0534_kaliraj
Remote router ID 81.5.5.5
BGP state = Established, up for 21:49:34
<snip>
Address family IPv4 Labeled-unicast: advertised and received
Address family VPNv4 Unicast: advertised and received
^C

## Slide 11: IOS-XR: screen capture (2/2)
RP/0/RP0/CPU0:ncs5508# show bgp vpnv4 unicast rd 81.1.2.2:16 81.2.2.2/32
Mon Nov 7 06:44:24.844 UTC
BGP routing table entry for 81.2.2.2/32, Route Distinguisher: 81.1.2.2:16
Versions:
Process bRIB/RIB SendTblVer
Speaker 37 37
Local Label: 24001
Last Modified: Nov 6 08:52:33.575 for 21:51:51
Paths: (2 available, best #1)
Advertised to peers (in unique update groups):
81.11.11.11
Path #1: Received by speaker 0
Advertised to peers (in unique update groups):
81.11.11.11
2
13.21.0.13 from 13.21.0.13 (81.5.5.5)
Received Label 33
Origin IGP, localpref 100, valid, external, best, group-best, import-candidate, not-in-vrf
Received Path ID 0, Local Path ID 0, version 37
Extended community: Color:100 0x0a02:0x00:0x00:0x00:0x00:0x00:0x64 RT:100:100

## Slide 12: References
IETF Draft: https://datatracker.ietf.org/doc/html/draft-ietf-idr-bgp-ct-00
https://community.cisco.com/t5/mpls/mpls-l3vpn-over-sr-te-policy/td-p/3777357